Laboratory chamber checks
Data acquisiton systems
Anna Toschi

---
Checks necessary before starting an experiment
Temperature
Work table stability
Security of the room

---
Components used
BOARD
Arduino UNO
INPUTS
1 Button
Temperature sensor KY-013
Ultrasonic sensor HC-SR04
Flame sensor KY-026
OUTPUTS
3 red LEDs
1 green LED

---
Time schedule

---
Temperature
TIME TABLE
4th May – 11th May
Estimated number of hours : 7.5
Effective number of hours: 10
TO DO
Understand sensor specifics and circuit implementation
ADC configuration
Calculation of the temperature
Look-up table
PROBLEMS
ADC configuration took longer than expected
Necessity to introduce look-up tables

---
Sensor: KY-013
NTC thermistor are made by semiconductive materials whose resistance decreases with the temperature: indeed by increasing the temperature the number of active charge carriers increases and the more charge carriers that are available, the more current a material can conduct.

---
Sensor: KY-013
NTC thermistor with a resistor of 10KΩ
Voltage Divider

---
Sensor: KY-013
The Steinhart–Hart equation links the resistance of the thermistor with the temperature:
A, B and C are the Steinhart-Hart coefficients which vary depending on the type and model of thermistor and the temperature range of interest.

---
Direct calculation of temperature
In principle by using the equations seen before, it is possible to calculate the temperature by measuring the voltage. However on Arduino complicated operations such as logarithms are not so efficient

---
Look-up tables
A look-up table is an array that replaces runtime computation with a simpler array indexing operation.
It is possible to build two arrays, one for the voltage and one for the corresponding temperature calculated by using the previous equations. For the other values it is possible then to make a linear interpolation.

---
Look-up tables
One curve is the one obtained by using the look-up table and for the other points using linear interpolation, while the other is obtained by using the equations.
The maximum error is for high temperatures.

---
Look-up tables
Pros
The computational cost is reduced
Cons
An error is introduced
Maximum error
0.86°C

---
Circuit implementation
SENSOR
1 pin to GROUND
1 pin to 5 V
1 pin to A1: analog input Arduino
LED
Cathode to GROUND
Anode connected through a resistor of 1kΩ to pin 6
It turns on if the temperature is higher than 40°C

---
Distance
TIME TABLE
27th May – 4th May
Estimated number of hours : 8
Effective number of hours: 10
TO DO
Understand sensor specifics and circuit implementation
Interrupts configuration
Calculation of the distance
PROBLEMS
Interrupts configuration took more than expected

---
Sensor: HC-SR04
It emits ultrasounds which travel through the air and if there is an object or obstacle on its path it will bounce back to the source.
When the Trigger pin is high the sensor creates an 8 cycle burst of ultrasound and when this ultrasonic signal finds an obstacle it is reflected towards the sensor.
Once the wave is returned after it getting reflected by any object the Echo pin goes high for a particular amount of time which will be equal to the time taken for the wave to return back to the sensor.

---
Input Capture Interrupts
To measure the distance between the obstacle and the sensor, the time in which the echo pin stays high is measured
The Input Capture mode of the Timer 1 of Arduino UNO is used. When a change of the logic level occurs on the input capture pin, the 16-bits value of the counter TCNT1 is written into the ICR1 register. By making the difference between the value of the counter when the echo pin gets high and when it gets low, the time of travel is measured.

---
Calculation of distance
The speed of sound depends on the temperature by the linear model:
Knowing the time interval and the speed of sound, the distance is simply the product of them divided by 2 since the sound crosses twice the same distance:

---
Circuit implementation
SENSOR
1 pin to GROUND
1 pin to 5 V
Trigger pin: pin 9
Echo pin: pin 8
LED
Cathode to GROUND
Anode connected through a resistor of 1kΩ to pin 3
It turns on if the distance is below 10 cm

---
Flame
TIME TABLE
15th May – 20th May
Estimated number of hours : 7.5
Effective number of hours: 6
TO DO
Understand sensor specifics and circuit implementation
Understand how to read a digital value using registers
PROBLEMS
Understand how the internal circuit works

---
Sensor: KY-026
Photodiode
Potentiometer
LM393 comparator
Outputs: A0 and D0. It has both an analogic and digital output

---
Circuit implementation
SENSOR
1 pin to GROUND
1 pin to 5 V
Digital pin: pin 2
LED
Cathode to GROUND
Anode connected through a resistor of 1kΩ to pin 4
It turns on if the digital pin becomes high

---
Alarm message
If the problem is solved and the button has been pressed after the LED turns on
Something went wrong
Everything is
 fine
If the temperature is too high or the distance too small or flame detected the LED turns off

---
Final circuit